## Slide 1: Supporting Diverse Dynamic Intent-based Policies using Janus
Anubhavnidhi “Archie” Abhashkumar*, Joon-Myung Kang#, Sujata Banerjee+,
Aditya Akella*, Ying Zhang o and Wenfei Wu^
This work was funded by Hewlett Packard Labs and done during internship program
*University of Wisconsin-Madison, # Hewlett Packard Labs, + VMware ,
o Facebook, ^ Tsinghua University

## Slide 2: Intent-based policies
Describes "what you want" instead of "what to do"

## Slide 3: Intent-based network policies: Reachability
Marketing must access database server and not access web servers
FW
IDS
Web Server
Database Server
Web
DB
Reachability

## Slide 4: Intent-based network policies: Waypoint
FW
IDS
IDS
Marketing must access database servers only through a firewall
Web Server
Database Server
DB
Reachability
Waypoint

## Slide 5: Intent-based network policies: Performance/QoS
Marketing must access database servers with minimum bandwidth of 100 mbps
Web Server
Database Server
50 mbps
100 mbps
100 mbps
100 mbps
50 mbps
100 mbps
DB
Reachability
Waypoint
QoS

## Slide 6: Intent-based network policies: Stateful Networks
H-IDS
L-IDS
L-IDS
Lightweight Intrusion Detection System (L-IDS) must forward traffic with more than 2 failed connection to Heavyweight IDS (H-IDS)
Web Server
Database Server
DB
DB
DB
Reachability
Waypoint
QoS
Stateful

## Slide 7: Intent-based network policies: Temporal (Time based)
FW
IDS
Marketing cannot access database servers from 5 pm to 9 am
Web Server
Database Server
9 am to 5 pm
DB
Reachability
Waypoint
QoS
Stateful
Temporal

## Slide 8: Intent-based network policies: Temporal (Time based)
FW
IDS
Marketing cannot access database servers from 5 pm to 9 am
Web Server
Database Server
5 pm to 9 am
DB
Reachability
Waypoint
QoS
Stateful
Temporal

## Slide 9: Intent-based network policies: Group based
FW
IDS
IDS
Marketing must access database servers only after going through an IDS with minimum bandwidth of 50 mbps
Marketing 1
Web Server
Database Server
50 mbps
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
DB
DB
Marketing 2
Reachability
Waypoint
QoS
Stateful
Temporal
Group
Notes: Intents introduced to simplify things. Representing as group does that

## Slide 10: Existing Works
Policies | PGA (Sigcomm’15) | Merlin (CoNext’14) | Kinetic (NSDI’15) | Janus
Group-based | ✔ | × | × | ✔
Reachability | ✔ | ✔ | ✔ | ✔
Waypoint | ✔ | ✔ | ✔ | ✔
Bandwidth | × | ✔ | × | ✔
Stateful | × | × | ✔ | ✔
Temporal | × | × | × | ✔
Policies | PGA (Sigcomm’15) | Merlin (CoNext’14) | Kinetic (NSDI’15)
Group-based | ✔ | × | ×
Reachability | ✔ | ✔ | ✔
Waypoint | ✔ | ✔ | ✔
Bandwidth | × | ✔ | ×
Stateful | × | × | ✔
Temporal | × | × | ×
Policies | PGA (Sigcomm’15) | Merlin (CoNext’14)
Group-based | ✔ | ×
Reachability | ✔ | ✔
Waypoint | ✔ | ✔
Bandwidth | × | ✔
Stateful | × | ×
Temporal | × | ×
Policies | PGA (Sigcomm’15)
Group-based | ✔
Reachability | ✔
Waypoint | ✔
Bandwidth | ×
Stateful | ×
Temporal | ×

## Slide 11: Janus: System Design

## Slide 12: Design Overview
Control Platforms (ex. POX, ONOS, etc.)
Best datapath configurations
host
host
Install rules
Get users input policies as graph
Get network topology and state info
Encodes policies & network as Integer Linear Program (ILP)
Install solution (paths) as rules in network
Janus
Policies
Network Topology
Notes: We extended policy graph model which is straighforward

## Slide 13: Challenge A: Group Atomicity
May not always satisfy all policies
Avoid partially configuring policies
Web
Mktg
min b/w: 50 mbps
DB
IT
min b/w: 50 mbps
FW
mktg1
mktg2
web1
db1
it1
s1
s2
s6
s4
s3
s5
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
70 mbps

## Slide 14: Challenge B: Avoid Excessive path changes
Choosing this path earlier would avoid an extra path change
Path change requires
Web
Mktg
min b/w: 100 mbps
DB
IT
min b/w: 100 mbps
IDS
100 mbps
mktg1
it1
db1
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
s1
s3
s4
s5
s6
s2
s7
100 mbps
web1
FW

## Slide 15: Challenge B: Avoid Excessive path changes
Choosing this path earlier would avoid an extra path change
Path change requires
  Changing switch rules
  Transferring NF states
Both incur significant overhead
100 mbps
mktg1
it1
db1
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
s1
s3
s4
s5
s6
s2
s7
100 mbps
web1

## Slide 16: Heuristics used in Janus
Configuring policies at group atomicity
Configuring stateful and temporal policies
Negotiating configuration of more policies
Notes: Algorithm/heuristic to configure these extensions
1. PGA semantics

## Slide 17: Configuring policies at group atomicity
Encode network topology and policy as constraints
Janus
Policies
Network Topology
host
host
mktg1
mktg2
web1
db1
it1
s1
s2
s6
s4
s3
s5
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
50 mbps
Path1
Path2
Path3
Solution recast to path-based
Policy satisfied at group granularity
ILP => Considers all paths as candidates
  Exponential with network size
  Long runtime
Janus => Consider X paths
Objective: Maximize no. of configured group policies
Best datapath configurations

## Slide 18: Configuring Stateful Policies
Every stateful policy has a default and non-default edge
2 types of constraints:
  default edge - hard constraints - must be satisfied
  non-default edge - soft constraints - can be satisfied but not at the expense of other hard constraints
Penalize violating soft constraints
Student
Web
failed connections
>=2
failed conn < 2
L-IDS
H-IDS

## Slide 19: Time-based joint optimization problem
Each time-period t has a separate Linear Program LP(t)
For each LP(t)
  Primary goal : configure all non-temporal policies and temporal policies valid at time t
  Secondary goal : reduce path changes that happen at other time period (~t)
    Objective: Maximize (no. of configured policies – penalty x no. of path changes)
This is a Joint optimization problem
Time: 1 to 9
Time: 9 to 14
Time: 14 to 1
Mktg
Web
IT
DB
IT
DB
min b/w: 50 mbps
Mktg
Web
IT
DB
min b/w: 50 mbps
Mktg
Web
min b/w: 100 mbps
min b/w: 100 mbps
min b/w: 50 mbps
min b/w: 50 mbps

## Slide 20: Greedy approach for configuring temporal policy
At time t(0)
  Non-temporal policies, Temporal policies valid for time t(0) : Hard Constraint
  Temporal policies valid for other time TP- t(0) : Soft Constraint
Remaining time periods t(r) = {TP- t(0)}
  Similar hard and soft constraint
  Additional objective: Minimize path changes from previous time period t(r-1)

## Slide 21: Negotiating configuration of more policies
Web
Mktg
min b/w: 20 mbps
FW
Time: 14 to 1
min b/w: 70 mbps
Time: 1 to 14
Janus makes binary decision :
  policy either gets its full bandwidth requirement
  (Or)
  not configured at all
Some links not fully utilized
DB
IT
min b/w: 50 mbps
mktg1
mktg2
web1
db1
it1
s1
s2
s6
s4
s3
s5
100 mbps
100 mbps
100 mbps
100 mbps
100 mbps
70 mbps
Time: 14 to 1
Negotiation: Policies reduce bandwidth requirement at bottleneck period and get compensated later
Web
Mktg
min b/w: 50 mbps
FW
Time: 0 to 24
Bottleneck period: 14 to 1
20 mbps Unused

## Slide 22: Negotiating configuration of more policies
Sensitivity analysis to detect set of bottleneck links
Find top K% policies based on bandwidth usage on bottleneck links
Find time period tb where K% policies can
    reduce their bandwidth at time period tb by N%
    increase their bandwidth at any time period ~tb by N%
Notify K% policies of proposed changes

## Slide 23: Implementation and Evaluation

## Slide 24: Implementation
Details
  Prototyped in Python and Pyretic
  Pyretic supports static and dynamic function boxes
  Uses POX to install rules in network
  Openflow can use queues to implement QoS policies
  Modified Pyretic and POX to install queue based rules
Control Platforms (ex. POX, ONOS, etc.)
Best datapath configurations
host
host
Install rules
Janus
Policies
Network Topology

## Slide 25
Experiment Setup
Use topologies from the Internet Topology Zoo dataset (http://www.topology-zoo.org/)
Randomly attach different endpoints and NFs to different nodes
Synthetically create our policy dataset
Use time and optimality gap as metrics
  Optimality gap - percentage difference between the number of policies satisfied by the original ILP and Janus.
Ran experiments on system with 32 cores, 2.4 GHz Intel Xeon Processor and 128 GB RAM

## Slide 26: Evaluation: How many candidate paths to consider?
Topology | Optimality Gap (%) |  | 
 | 10 Paths | 5 Paths | 2 Paths
Ans(18) | 0.6 | 10.3 | 23.2
Agis(25) | 0 | 0 | 14.6
CrlNetServ(33) | 0.9 | 10.7 | 25.8
Cwix(36) | 0 | 4 | 19.8
Garr201008(36) | 0 | 3.3 | 12.4
Topology | Percentage reduction in Time (%) |  | 
 | 10 Paths | 5 Paths | 2 Paths
Ans(18) | 77.4 | 93.8 | 97.3
Agis(25) | 49 | 61 | 88.9
CrlNetServ(33) | 37.8 | 66.8 | 87.9
Cwix(36) | 42 | 58.5 | 87.4
Garr201008(36) | 97 | 99 | 99
Topology | Optimality Gap (%) |  | 
 | 10 Paths | 5 Paths | 2 Paths
Ans(18) | 0.6 | 10.3 | 23.2
Agis(25) | 0 | 0 | 14.6
CrlNetServ(33) | 0.9 | 10.7 | 25.8
Cwix(36) | 0 | 4 | 19.8
Garr201008(36) | 0 | 3.3 | 12.4
Topology | Percentage reduction in Time (%) |  | 
 | 10 Paths | 5 Paths | 2 Paths
Ans(18) | 77.4 | 93.8 | 97.3
Agis(25) | 49 | 61 | 88.9
CrlNetServ(33) | 37.8 | 66.8 | 87.9
Cwix(36) | 42 | 58.5 | 87.4
Garr201008(36) | 97 | 99 | 99
# of policies = 1000
# of endpoints per policy = 40
# of hosts = 40000

## Slide 27: Evaluation: Penalty for Soft constraints
φ = 0.2 satisfies all default and 30 to 70 % non-default policies
φ = penalty weight to violate soft constraint

## Slide 28: Evaluation: Configuring temporal policies
Spread policies across 5 time periods
Set penalty weight for path change = 0.2
Joint optimization algorithm runtime > 20 hours
No. of Policies | No. of Configured Policies | Reduction in Path changes(%) | Time(s)
500 | 500 | 98.2 | 492
600 | 600 | 94.7 | 675
700 | 691 | 92.6 | 1438
800 | 741 | 91.3 | 4157
No. of Policies | No. of Configured Policies | Reduction in Path changes(%) | Time(s)
500 | 500 | 98.2 | 492
600 | 600 | 94.7 | 675
700 | 691 | 92.6 | 1438
800 | 741 | 91.3 | 4157
No. of Policies | No. of Configured Policies | Reduction in Path changes(%) | Time(s)
500 | 500 | 98.2 | 492
600 | 600 | 94.7 | 675
700 | 691 | 92.6 | 1438
800 | 741 | 91.3 | 4157

## Slide 29: Evaluation: Negotiation to configure more policies
Configure 600 policies across 4 time periods
Without negotiation => configure 536 policies
When N > 5%, number of negotiable policies decreases due to lack of extra bandwidth at other time periods
After K = 60%, increase in number of extra policies configured is not significant

## Slide 30: Extension, Future Work and Conclusion

## Slide 31: Extension to other QoS metrics
Jitter
  Use multi-level priority queues
  Queue level assigned based on jitter policy
Latency
  Number of hops as a proxy for latency
Need Support for other performance/QoS metrics
Notes: Partial extension

## Slide 32: Future Work: Fast/consistent bulk rule update
Fast/consistent bulk rule update
  Issues:
    Maintain consistency during rule update
    Fast rule update to reduce downtime
  Integrate existing solutions : Dionysus (Sigcomm ’14) and McClurg et al’s automated update synthesis (PLDI’15)

## Slide 33: Conclusion
Proposed Janus, a system to configure QoS and dynamic intent-based policies at group granularity
Developed variety of novel heuristic algorithms which maximize the number of configured policies and minimize the number of path changes
Offer near optimal solution in a reasonable amount of time for several network topologies and scenarios

## Slide 34: Backup Slides

## Slide 35: Use Policy Graph Abstractions (PGA) to specify Intents
Why we chose PGA?
Network policies intuitively represented as graphs
Compose policies from different policy writers
Used in real life systems like OpenDaylight
DB
Marketing
IDS
DB
Marketing
FW
DB
Marketing
Notes: OpenDaylight Network Intent Composition project

## Slide 36: Extension to Policy Graphs
Marketing
Web
9am – 6pm
min b/w: low
6pm – 5am
min b/w: high
IDS
FW
FW
Add QoS and State as edge property
Web
Marketing
tcp:80
Web
Marketing
tcp:80
min b/w: high
(200 mbps)
Marketing
Web
failed connections
>=4
failed conn < 4
L-IDS
H-IDS
Composing policies is straightforward [Details are in paper]

## Slide 37: Evaluation: ILP VS Janus with 5 candidate paths
Each policy has 20 endpoints
With bandwidth requirement 10 to 30 mbps
0 Optimality Gap
2x difference in magnitude