## Slide 1: Tiramisu: Fast Multilayer Network Verification
Anubhavnidhi “Archie” Abhashkumar*, Aaron Gember Jacobson#,
and Aditya Akella*
*University of Wisconsin-Madison, # Colgate University

## Slide 2: Distributed Control Planes
D
C
B
Z
Y
E
Policies
Y  Z
Configuration Example
interface GigabitEthernet0/1
  ip address 1.0.1.1 255.255.0.0
  ip ospf cost 1
router ospf 10
  network 3.0.1.2 0.0.255.255 area 0
OSPF
OSPF
OSPF
OSPF
1
1
Z
1
Notes: Vast networks use control planes that run multiple protocols to satisfy network policies
Protocols compute route that implement policies
Flow adheres the policy

## Slide 3: Router Configurations are Complex
interface GigabitEthernet0/1
ip address 1.0.1.1 255.255.0.0
ip ospf cost 1
!
interface GigabitEthernet0/2
ip address 10.11.11.1 255.255.0.0
!
router bgp 300
neighbor 2.2.2.2 route-map COMM out
!
route-map COMM permit 10
set community 1:1 additive
set local-preference 150
!
router ospf 10
network 3.0.1.2 0.0.255.255 area 0
Multiple routing protocols
  BGP
  OSPF
  …
Multiple routing metrics
  ospf cost
  local preference
  …
Multiple filters
  Community
  …

## Slide 4: Configuration Complexity Make Errors Common
Verification tools can proactively check for failures
Policy violations manifest under failures

## Slide 5: Multiple Network Verification tools
Performance
Coverage
Bagpipe
(OOPSLA’16)
Plankton
(NSDI’20)
Minesweeper
(SIGCOMM ’17)
ERA
(OSDI’16)
Batfish
(NSDI’15)
ARC
(SIGCOMM’16)
P-REX
(CONEXT’18)
Goal: A verification tool that has good coverage and good performance
Tiramisu
(NSDI’20)
Notes: Add tiramisu with animnation

## Slide 6: Performance VS Coverage
ARC (SIGCOMM’16)
  Graph algorithms
Network
configurations
2
2
4
1
0
6
Weighted Graphs
Minesweeper (SIGCOMM’17)
  Symbolic encoding
Network configurations
Routing Algorithms
Policies
SMT Constraints
Z3 solver
Notes: First iBGP examples
ARC – cannot verify - Cannot model iBGP, community, local-preference, etc
\
Minesweeper – slow
Then Slide 9
Aaron: O(n) for dfs

## Slide 7: Cross Layer Dependency
B
E
C
iBGP
iBGP
eBGP
eBGP
1
D
iBGP
OSPF
OSPF
OSPF
1
5
Y
Z
Dst | NextHop
E | B
B | B
D | D
Dst | NextHop
E | E
C | C
D | D
Dst | NextHop
B | B
C | C
ROUTER C
ROUTER B
ROUTER D
IBGP uses OSPF computed route to reach next hop router
C  E
Cross Layer Dependency: iBGP - OSPF
Notes: Words to say green is depenedent on OSPF/orange

## Slide 8: Cross Layer Dependency
B
E
C
iBGP
iBGP
eBGP
eBGP
1
D
iBGP
OSPF
OSPF
OSPF
1
5
Y
Z
Dst | NextHop
E | B
B | B
D | D
Dst | NextHop
E | E
C | C
D | D
Dst | NextHop
B | B
C | C
ROUTER C
ROUTER B
ROUTER D
Dst | NextHop
E | B
B | D
D | D
E

## Slide 9: ARC and Minesweeper
Minesweeper (SIGCOMM’17)
ARC (SIGCOMM’16)
Ebgp
Bbgp
Bospf
Cospf
Cospf
…….
192.0.0.0 ≤ out.prefix
out.prefix ≤ 192.1.0.0
out.valid ⇒ true
best.valid ⇒ out.lp = 120
best.valid ⇒ out.ad = 20
…….
…….
192.0.0.0 ≤ out.prefix
out.prefix ≤ 192.1.0.0
out.valid ⇒ true
best.valid ⇒ out.lp = 120
best.valid ⇒ out.ad = 20
…….
…….
192.0.0.0 ≤ out.prefix
out.prefix ≤ 192.1.0.0
out.valid ⇒ true
best.valid ⇒ out.lp = 120
best.valid ⇒ out.ad = 20
…….
  Insufficient feature coverage
    No IBGP, local preference, community, ….
  Poor performance
    replicate model for iBGP
Notes: I have used iBGP as example, this extends to VLANs, etc.
Likewise Minesweeper specify poor performance – all policies require full model

## Slide 10: Insights
Configurations
Configurations
NETWORK
MODEL
VERIFICATION
ALGORITHMS
NETWORK
MODEL
VERIFICATION
ALGORITHM-1
VERIFICATION
ALGORITHM-2
VERIFICATION
ALGORITHM-N
….
B
C
1
D
OSPF
OSPF
OSPF
1
5
S1
Policy 1: Which path is preferred?
C→B << C→D→B
PATH
ENUMERATION
Policy 2: Can C reach B with 1 link failure?
QUANTITATIVE GRAPH PROPERTY
Policy 3: Is C always unreachable/blocked from B?
PATH
EXISTENCE
(CONNECTIVITY)
C→B : ospf cost = 1
C→D→B : ospf cost = 6
Min-cut = 2
B
B
B
 | Model | Verification
ARC | Graph | Graph
Minesweeper | SMT | SMT
low coverage
high coverage
low performance
high performance
low performance
high fidelity
high performance
low fidelity
  Multilayer graph with
  vector of edge weights
  Categories policies based on fidelity
Insight 1: Decouple network encoding from verification algorithm
Insight 2: Different properties require different levels of fidelity modeling of the control plane. Use property-specific algorithm for performance benefits
Notes: Italize the operators in <<

## Slide 11: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
TDFS
PATH
ENUMERATION
NUMERIC GRAPH PROPERTY
PATH
EXISTENCE
Graph
Model
Algorithms
ILP
TPVP

## Slide 12: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
Graph
Model

## Slide 13: Traffic Propagation Graph (TPG)
Vertices: RIB of a routing processes and ingress/egress point of a switch/router
Edges: establish route dependency and traffic flow
Vector of edge weights: multiple route metrics
Bvlan:BC:in
Z
Bvlan:BD:in
Evlan:BE:in
Bospf
Cospf
Dospf
Ebgp
Bbgp
Cbgp
Dbgp
Y
Evlan:BE:out
Bvlan:BD:out
Bvlan:BE:in
Cvlan:BC:in
Cvlan:BC:out
Cvlan:CD:in
Cvlan:CD:out
Dvlan:CD:in
Dvlan:CD:out
Dvlan:BD:in
Bvlan:BC:out
<ospf:1>
<ospf:1>
<len:0>
<len:0>
<ospf:5>
<len:0>
<len:1>
<ospf:5>
<ospf:1>
Dvlan:BD:out
Bvlan:BE:out
B
E
C
iBGP
iBGP
eBGP
eBGP
1
D
iBGP
OSPF
OSPF
OSPF
1
5
Y
Z
Notes: Aaron: Intuition could be represented as detailed packet flow animation

## Slide 14: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
PATH
ENUMERATION
Graph
Model
Algorithms
TPVP

## Slide 15: TPVP - Tiramisu Path Vector Protocol
Griffin et al. (TON’2002) and Sobrinho (TON’2005) models stable paths problem as Simple Path Vector Protocol (SPVP) and routing algebra
TPVP is derived from SPVP and is modeled on routing algebra
  ⊕ operator to model path cost computation
  ⪯ operator to model preference relation and path selection
Cospf
<ospf:1>
<ospf:1>
<len:0>
Cbgp
{ospf:5}
{ospf:1}
{ospf:2}
Node | ⊕ | ⪯
Cospf | {ospf:1} ⊕ospf {ospf:5} = {ospf:6} | {ospf:6} ⪯ ospf {}
Node | ⊕ | ⪯
Cospf | {ospf:1} ⊕ospf {ospf:1} = {ospf:2} | {ospf:2} ⪯ ospf {ospf:6}
{ospf:6}
{ospf:2}
{len:0, ospf:2}
Node | ⊕ | ⪯
Cbgp | {len:0} ⊕bgp {ospf:1} = {len:0, ospf: 2} | {len:0, ospf:2} ⪯ bgp {}
{ospf:5}
Node | ⊕ | ⪯
Cospf | {ospf:1} ⊕ospf {ospf:5} = {ospf: 6} | {ospf:6} ⪯ ospf {ospf:2}
{ospf:5}
{}
{}
Notes: This repeats till the path converges

## Slide 16: TPVP - Tiramisu Path Vector Protocol
To verify path preference (P1 << P2), Tiramisu multiple instances of TPVP for different failure scenarios
Runs TPVP three times
B
C
1
D
OSPF
OSPF
OSPF
4
1
S1
P1: C→D→B : ospf cost = 2
P2: C→B : ospf cost = 4
Notes: This repeats till the path converges

## Slide 17: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
NUMERIC GRAPH PROPERTY
Graph
Model
Algorithms
ILP

## Slide 18: ILPs - Integer Linear Programs
Traffic flows in the direction opposite to route advertisement
Only depends on quantitative path property and not exact path
ILP constraints model reachability
  Tag/Community
Objective models the graph property
More details about the ILP and its corner cases are in the paper
min cut is 1
B
C
D
eBGP
eBGP
eBGP
S1
<at:c1>
<bt:c1>
B
B
    Reachability < K failures = Minimize link failures
    Longest path = Maximize path length
Notes: Have a text on that slide about advertisement is opposite to traffic

## Slide 19: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
TDFS
PATH
EXISTENCE
Graph
Model
Algorithms

## Slide 20: TDFS – Tiramisu Depth First Search
B
C
D
eBGP
eBGP
eBGP
S1
<bt:c1>
<rt:c1>
<at:c1>
Verify if src and dst are always unreachable
Can’t use vanilla graph algorithms to model tags
Conditions
  Block path: tag-blocking node  tag-adding node
  Allow path: tag-blocking node  tag-removing node  tag-adding node
Notes: Have text Can’t use vanilla DFS

## Slide 21: Tiramisu Overview
Traffic Propagation Graph (TPG)
Routing Adjacencies Graph (RAG)
Configurations
TDFS
PATH
ENUMERATION
NUMERIC GRAPH PROPERTY
PATH
EXISTENCE
Graph
Model
Algorithms
ILP
TPVP

## Slide 22: Evaluation
Networks used
  Real networks: 4 universities and 34 datacenters
Evaluation
  Tiramisu verification performance
  Comparison with other state-of-the-art
Policy | Name | Algorithm
block | Always blocked | TDFS
bound | Always bounded length | ILP
pref | Path preference | TPVP
Notes: Reduce to 3 policy

## Slide 23: Evaluation – Tiramisu’s Performance
bound is slowest because it uses ILP
block is fastest because it uses TDFS
pref is slower than block as TPVP is more complex
Why does pref seem faster than ILP?
For large networks, pref is as long as bound
  Large networks  More candidate and longer paths  More calls to TPVP
Chart: University
| Uni1 (9) | Uni2 (24) | Uni3 (26) | Uni4 (35)
pref | 7 | 61 | 42 | 29
bound | 26 | 71 | 58.38 | 40.08
block | 1.15 | 2.6 | 2.3 | 2.5
Notes: Preface it with a question – why does TPVP seem faster?

## Slide 24: Evaluation: Tiramisu vs. Minesweeper (No failures)
block has the most speedup
pref has the least speedup (especially for large networks)
  Large networks  more and longer candidate paths  more calls to TPVP
Chart: pref
| 2 | 4 | 7 | 7 | 8 | 8 | 8 | 10 | 11 | 11 | 11 | 12 | 12 | 20 | 21 | 22 | 22
Speedup | 34.5 | 29.1 | 29.6 | 32.1 | 20.1 | 12.4 | 18.3 | 28.2 | 21.1 | 17.6 | 20.8 | 18.2 | 28.8 | 7.7 | 13.3 | 8.5 | 15.3
Chart: bound
| 2 | 2 | 5 | 6 | 6 | 6 | 7 | 7 | 8 | 8 | 8 | 10 | 10 | 11 | 11 | 11 | 11 | 12 | 12 | 15 | 20 | 20 | 20 | 21 | 21 | 22 | 22 | 24
Speedup | 9.5 | 6 | 9.9 | 12.4 | 12.4 | 13.5 | 18.3 | 15.8 | 20.1 | 19.7 | 19.3 | 21.8 | 12 | 20 | 19.6 | 21.1 | 19.6 | 20 | 20.1 | 20.2 | 26.5 | 24.6 | 22.5 | 19 | 18.7 | 22.9 | 22.6 | 24.8
Chart: block
| 2 | 2 | 5 | 6 | 6 | 6 | 7 | 7 | 8 | 8 | 8 | 10 | 10 | 11 | 11 | 11 | 11 | 11 | 12 | 12 | 15 | 20 | 20 | 20 | 21 | 21 | 22 | 22 | 24
Speedup | 54.6 | 38.1 | 13.8 | 14.4 | 14.4 | 15.4 | 22.3 | 17.7 | 62 | 55.8 | 56.4 | 74.7 | 15.4 | 69.2 | 71.3 | 78.6 | 79.6 | 70.5 | 88.1 | 78 | 100.8 | 119.9 | 132.4 | 98 | 119.4 | 102.1 | 116.2 | 114.7 | 139.8

## Slide 25: Evaluation: Tiramisu vs. Minesweeper (All failures)
Same trend but significantly better speed up
Minesweeper uses same encoding for all policies
Tiramisu uses property specific algorithms
Chart: pref
| 2 | 4 | 6 | 7 | 7 | 8 | 8 | 8 | 10 | 11 | 11 | 11 | 12 | 12 | 20 | 21 | 22 | 22
Speedup | 91.85 | 30.37 | 53.06 | 66.73 | 50.2 | 33.3 | 24.5 | 21.35 | 65.59 | 39.29 | 34.1 | 32.81 | 37.31 | 39.81 | 31.52 | 28.92 | 27.82 | 31.41
Chart: bound
| 2 | 2 | 2 | 4 | 5 | 6 | 6 | 6 | 7 | 7 | 8 | 8 | 8 | 8 | 10 | 10 | 11 | 11 | 11 | 11 | 11 | 12 | 12 | 13 | 15 | 20 | 20 | 20 | 21 | 21 | 22 | 22 | 22 | 24
Speedup | 1 | 8 | 1 | 5 | 2 | 2 | 3 | 3 | 4 | 3 | 13 | 12 | 11 | 10 | 19 | 3 | 20 | 16 | 18 | 18 | 20 | 24 | 15 | 4 | 29 | 33 | 44 | 30 | 41 | 28 | 34 | 39 | 45 | 50
Chart: block
| 2 | 2 | 2 | 4 | 5 | 6 | 6 | 6 | 7 | 7 | 8 | 8 | 8 | 8 | 10 | 10 | 11 | 11 | 11 | 11 | 11 | 12 | 12 | 13 | 15 | 20 | 20 | 20 | 21 | 21 | 22 | 22 | 22 | 24
Speedup | 20 | 84 | 10 | 55 | 25 | 22 | 34 | 40 | 30 | 30 | 115 | 138 | 134 | 114 | 218 | 33 | 271 | 201 | 218 | 191 | 141 | 206 | 267 | 35 | 285 | 529 | 629 | 401 | 590 | 630 | 456 | 688 | 383 | 590
Notes: Add thois text Emphasize minesweeper used general SMT encoding whereas we used property-specific verification algorithms

## Slide 26: Summary
Tiramisu decouples encoding of the network from verification algorithms
Tiramisu uses a multilayer graph control plane model
Tiramisu uses
  TPVP to enumerate paths
  ILP to measure quantitative graph property
  TDFS to check path existence
Tiramisu achieves good performance without losing too much coverage
  No external advertisements